## Slide 1: Constructing a digital 3D road network for The Netherlands
Kristof Kenesei K.Kenesei@student.tudelft.nl
Supervisors: 1st – Ravi Peters 2nd – Jantien Stoter 2021-06-22
MSc Thesis Defence
Notes: Welcome to my thesis defence. The title of my graduation project is “Constructing a digital 3D road network for The Netherlands”.

## Slide 2: Agenda
Motivation and background
Processing pipeline
Final results and accuracy
Comparison with commercial results
Conclusions
Constructing a digital 3D road network for The Netherlands
Notes: Agenda of the presentation will be:
  Motivation and some background
  Details of the pipeline design and showcase of intermediate results
  Final results and accuracy assessment
  Outcome of comparison with the commercial results
  Concluding remarks

## Slide 3: What is NWB?
Stands for Nationaal Wegenbestand
Produced and maintained by Rijkswaterstaat via NDW (Nationaal Dataportaal Wegverkeer)
  Commercial “client” of this project
Open data geospatial product of The Netherlands
Graph-like representation of all named roads in the country
https://nationaalwegenbestand.nl/wat-het-nwb
Motivation and background
Notes: Full name is Nationaal Wegenbestand, which stands for national road product
Open data geospatial product of The Netherlands
Produced and maintained by NDW
  They are the commercial “client” of this project
Graph-like representation of all named roads in The Netherlands
  Knooppunten: real-life intersections, i.e. graph nodes
  Wegwakken: road centreline segments, i.e. graph edges

## Slide 4: Purpose of georeferencing
In general:
  We can relate the road to its physical surroundings – required in many applications
In this specific case:
  This project is relevant to noise modelling
   Need to know the geographical source of noise
http://www.noisemap.ltd.uk/wpress/features/roads/
Motivation and background
Notes: Georeferencing allows us to relate roads to their surroundings
  I.e. to correlate with external information, such as addresses in route planning
Our scenario: NWB is a traffic noise source in a noise propagation model
  Position relative to surrounding objects needs to be known
  Otherwise the noise load on the objects cannot be determined

## Slide 5: Justifying 3D georeferencing
Motivation and background
Notes: Traffic noise modelling traditionally done in 2D, but these are not very realistic
A 3D noise propagation model should use a 3D road network
Consider the example:
  This is a best case scenario, we already have a terrain model and 3D buildings
  If we model the road to always lie on the terrain, then the hill (part of the terrain) will block the noise
  If we consider that it is in fact an elevated road, some of the noise will propagate to the building
New noise legislations in The Netherlands prescribe a 3D model

## Slide 6: Essence of problem
https://www.researchgate.net/figure/A-2D-Road-Segment-With-its-Neighborhood-Definition-2-A-3D-spatial-network-is-also_fig2_236964742
How do we get from here…
…to here?
Motivation and background
Notes: So how do we get from a 2D road network (graph) to a 3D road network?
In other words, how do we enrich NWB with elevation data?

## Slide 7: Constraints
Comply with accuracy requirements
Use existing open-data elevation measurements
Explore academic aspects, not just fulfil a commission
Preserve topology, keep original 2D georeferencing
Try to improve upon the methods of the commercial implementation
Motivation and background
Notes: In addition to the base problem, there are a few constraints
  Noise regulations prescribe a 20 cm minimum accuracy at 2 STDs
  We wish to use open data datasets only
  Explore academic aspects, not only complete a commercial commission
  Preserve topology, keep the 2D georeferencing
  Compare with, and try to improve upon, the commercial implementation
    Was developed in parallel with academic project

## Slide 8: Research question
“How can we achieve a 3D conversion of the NWB dataset using Dutch open geospatial data and primarily 2.5D-based surface modelling methods, while guaranteeing optimal and quantifiable accuracy and completeness?”
Motivation and background
Notes: In the end we came up with the research question:
“How can we achieve a 3D conversion of the NWB dataset using Dutch open geospatial data and primarily 2.5D-based surface modelling methods, while guaranteeing optimal and quantifiable accuracy and completeness?”
2.5D-based surface modelling and scientific accuracy assessment are mentioned specifically because these are the main added academic aspects

## Slide 9: The datasets
NWB motorways (green), provincial roads (brown)
AHN3 points (blue to green points), DTB line features (red lines)
2D
3D
“… using Dutch open geospatial data …”
Processing pipeline
Notes: The datasets are:
  NWB – needs to be converted to 3D
  We are only interested in motorways and provincial roads
AHN3 – the Dutch national remote sensing dataset
  Cannot penetrate objects that are opaque to light
  Difficult to sense 3D relationships due to this
  Feature extraction is necessary, which is never perfectly accurate
DTB – a road management dataset of The Netherlands
  We use the road marking line models from this dataset
  This can provide coverage in AHN3 gaps
  Coverage is limited, and it only exists for motorways
Highlighted the relevant part of the main research question

## Slide 10: Overview of pipeline steps
Mosaicked together from methods found in literature, and own ideas
Made surface modelling a core stage of NWB’s 3D conversion
“… primarily 2.5D-based surface modelling methods …”
Processing pipeline
Notes: This flowchart shows our planned processing pipeline
Result of a preparation process that spanned about two months
  Performed the necessary literature review
  Consulted with NDW and their commercial developer
  Mosaicked together the procedure based on the above, and my own ideas
  Made the generation of road surface TIN models a core stage
    Producing surface models is for research purposes only
Highlighted the relevant part of the main research question

## Slide 11: NBRS generation
NBRS generation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
Issue: various workflow steps would work best with subdivisions of NWB
Solution: “split” NWB into Non-Branching Road Segments (NBRS)
  Maximise length, minimise internal angles, disallow self-intersection
Processing pipeline
Input NWB geometry
Generated NBRS geometries (each colour represents an NBRS)
Notes: First step of the pipeline: NBRS generation
Subdivide NWB into well-behaved segments, a prerequisite for various subsequent steps
  I call these Non-Branching Road Segments or NBRSs for short
How exactly do we generate NBRSs?
  NBRS are assembled from connected wegvakken (the building blocks of NWB)
  The algorithms try to maximise length and minimise internal angles
  Self-intersections are not allowed – 2.5D modelling is made possible
Implemented two algorithms
  “Geometric” algorithm relies only on NWB geometry
  “Semantic” algorithm uses attribute data too, but is thus specialised to NWB

## Slide 12: Lidar segmentation
Idea during implementation: quickly estimate rough elevations prior to this step (Hypothesis: it will improve segmentation effectiveness)
NBRS generation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
Issue: handling entire point cloud at once is both inefficient and ineffective
Solution: segment point cloud into subclouds with points relevant to each NBRS
Processing pipeline
Notes: What is Lidar segmentation?
  In our case, it means the selection and grouping of Lidar points…
  …that are relevant to the underlying road surface of each NBRS
Why do we need Lidar segmentation?
  In short: to improve performance and make subsequent steps more effective
Starting from a 2D road network limits effectiveness  try to first create a rough 3D conversion of NWB

## Slide 13: Elevation estimation
Issue: Lidar segmentation may be more efficient using approximate road elevations
Solution: perform a rough, very quick 3D conversion of NWB
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
3D-converted NBRS geometries
Side view
Top view
AHN3 point cloud
+
2D NBRS geometries
Processing pipeline
Notes: Added a step to the pipeline: elevation estimation
The goal is to extract elevations for NWB from AHN3
  As quickly as possible
  And keeping the algorithm relatively simple
Really just to provide a starting point for later steps

## Slide 14: Elevation estimation
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
Processing pipeline
Notes: The implemented workflow is simple:
  Densify vertices where necessary
    It means the addition of vertices where line segments are very long
    Allows us to better sample the elevation data
  At each NWB vertex, query AHN3 for nearby points and derive an elevation value
    Red vertices/lines in figure
  Fit polynomials on the 2D profiles represented by each NBRS to identify outliers
    Illustrated by green line
  Interpolate new values for the outliers via linear interpolation
    Blue vertices and lines
The results are surprisingly accurate wherever the elevation profiles of the roads are relatively simple

## Slide 15: Lidar segmentation
Issue: handling entire point cloud at once is both inefficient and ineffective
Solution: segment point cloud into subclouds with points relevant to each NBRS
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
AHN3 point cloud, DTB lines
+
3D NBRS geometries
Subclouds
Processing pipeline
Notes: Next step in pipeline: Lidar segmentation
The preliminary elevations proved to indeed be useful
  Thanks to them, less irrelevant Lidar points are examined in complex areas
DTB is used in conjunction with AHN3
  It is used both as an elevation source, and as reference (like the 3D centrelines)

## Slide 16: Lidar segmentation
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
Processing pipeline
Notes: Workflow:
  Fit planes on point cloud points close to each NBRS vertex
    3D squares and red vertices/lines in illustration, respectively
  For each vertex, pre-select close-by points that conform with local plane fit
    Not shown here
  Progressing along NBRS vertices, detect shifts in the planes
    Such as the transitional plane illustrated here
  If DTB can be used to disambiguate, make use of it
    Such as underneath the bridge here
    Also use its (densified) vertices where reliable
  Accept planes (and conformant points) which agree with the global trend of the NBRS
     Assemble the subclouds
Detecting transitional plane fits was key, and also the most challenging task

## Slide 17: Edge estimation
Issue: we need seed contours for active contour optimisation
Solution: generate seed contours (= edge estimates) by inspecting cross-section trends
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
Subclouds
2D NBRS geometries
+
Processing pipeline
Notes: Next step in pipeline: edge approximation
We are looking for 3D lines that approximately delineate the smooth, traffic-occupied parts of roads.
  These were originally going to be optimised in the next pipeline step
Key part of original plan to accurately classify road surface reflections

## Slide 18: Edge estimation
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
Processing pipeline
Notes: Workflow:
  Construct cross-sections on NBRS vertices and densify them
    Black vertices and lines in inset
  Compute elevations for them from nearby part of relevant subcloud
    Not shown here
  Select suitable edge points on both sides of NBRS from inliers based on line fit
    Dashed blue line
  Discard non-conformant cross-sections
    Dashed red lines
  Assemble preliminary edges of NBRS from these discrete edge points
    Green lines
Dealing with NWB getting close to road edges was the most challenging aspect
  Shown in illustration
  This is due to NWB’s coarse/inaccurate 2D georeferencing

## Slide 19: Edge optimisation
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
Edge optimisation
Issue: preliminary edges are angular, often do not cover the whole road surface
Solution: iteratively improve edges using active contour optimisation (snakes)
Attractor maps
Preliminary edges
Optimised edges
+
Subclouds
Processing pipeline
Notes: Next step in pipeline: edge optimisation
This was a core part of the original pipeline design
  The original intention was to generate rough preliminary edges…
  …then optimise them using active contour optimisation…
  …to thus be able to select road surface reflections with near-perfect accuracy
Workflow:
  Construct attractor maps for each NBRS
    They are rasters that describe how smooth the Lidar-defined surface is locally
  Run active contour optimisation for each NBRS, inputting the attractor maps and preliminary edges

## Slide 20: Edge optimisation
Issues during implementation: active contour optimisation does not perform well enough.  Made it optional in the final pipeline configuration.
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
Edge optimisation
Edge not in raster / too far
Perturbation due to vehicles
Ideal edges
Contour not on road
Processing pipeline
Notes: This did not pan out as well as I was hoping
Using conventional active contour optimisation, some edges are drawn too far inwards or outwards
Imperfect attractor maps result in disruptive artefacts
Difficult to find a parametrisation that works in all possible scenarios
I only found implementations of basic active contour optimisation, not advanced ones
I eventually decided to phase out edge optimisation (made it optional, it can still be used)
  Research timeframe did not allow me to spend more time on this
  Required significant modifications to the edge estimation and TIN construction steps

## Slide 21: TIN construction
Issue: need to create an efficient interpolation structure to obtain final elevations
  Also: academic desire to model road surfaces
Solution: build TIN models from subcloud points incrementally
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
Subclouds
Preliminary edges
OR
Optimised edges
TIN road surface models
Processing pipeline
Notes: Next step in pipeline: TIN construction
Need to create an interpolation structure from where elevations for NWB can be extracted effectively
  Also want to model road surfaces – why not do both in a single step?
Original intention was to just construct a CDT using the optimised edges and the Lidar points between them
After phasing out edge optimisation, it was necessary to do this differently
  The TINs are now constructed incrementally, via a surface growing process

## Slide 22: TIN construction
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
Processing pipeline
Notes: Workflow:
  Seed the TIN using points close to the skeleton of road edges
    Green line and green points, edges shown as red lines
  Grow the TIN within the edges using an algorithm inspired by TIN-based ground filtering workflows
    Normal conditional insertions are shown as red points, insertions take place if point conforms with local triangle
    Growing-type insertions are shown as yellow points, these inspect the local planar trend in a larger area
  Extend the TIN beyond the edges using targeted conditional insertions between extension boundaries (optional)
    For instance, in extension 3, Lidar points between the blue lines labelled “Extension 3” and “Extension 4” would be considered
    Can help fill areas missed by the previous step, such as hard shoulders

## Slide 23: Elevation interpolation
Issue: need to convert NWB to 3D based on the surface models
Solution:
  Interpolate NWB vertices in the TINs of each NBRS
  Where TIN does not exist, use linear interpolation as a post-processing step
NBRS generation
Elevation estimation
Lidar segmentation
Edge estimation
TIN construction
Elevation interpolation
TIN-linear interpolation background
Weight of leftmost vertex
Figures from:
Fan, L., Smethurst, J., P.M., A., and Powrie, W. (2014), Propagation of vertical and horizontal source data errors into a tin with linear interpolation. International, Journal of Geographical Information Science, 28:1378–1400.
Processing pipeline
Notes: Next step in pipeline: elevation interpolation
Workflow:
  Interpolate NBRS vertex elevations in corresponding TINs
  Take care to ensure continuity in intersections across NBRS
  Interpolate missing values linearly where the TINs do not exist locally
    As a post-processing step
Using the TIN-linear interpolator
  The points are projected onto the triangle’s surface, in which they are found
The weight of each triangle vertex decreases away from it, as shown in the figure
The output file is identical to the input in every aspect other than the added Z coordinates

## Slide 24: Comparison with preliminary elevations
Continuity enforcement
Final (colour-coded) and preliminary (brown) 3D-NWB geometry
Final results and accuracy
Notes: The final elevations represent an improvement relative to the preliminary 3D geometries
  The final 3D centrelines are more realistic where curvature is complex
  Continuity is now being enforced
Less smooth, because each elevation is based on exactly three Lidar points, rather than a patch

## Slide 25: Comparison with subclouds
Linear interpolation
DTB-based TIN-linear interpolation
AHN3-based TIN-linear interpolation
“Hanging bridges” due to switching between AHN3 and DTB
Subclouds and final 3D-NWB geometry
Final results and accuracy
Notes: Comparison of the final 3D-NWB geometries and the subclouds
Switching between AHN3 and DTB can be spotted
  Even where very little difference exists between two datasets
Where AHN3 data is available, the final 3D-NWB geometry is fully defined by it
Linear interpolation reasonable where no DTB data is available and the gaps are small

## Slide 26: Completeness of TINs
Final results and accuracy
Final TINs and paved surface extents (BGT)
Edges of paved areas
Final TINs
NWB is close to road edge
Notes: Current pipeline does not allow the paved surfaces to be fully modelled
  This was my original goal
Approximately 75% of the paved surfaces are modelled
  Here this is slightly lower, as motorways are very wide
  For provincial roads it can be above 90%
Traffic-occupied surfaces are fully covered under normal circumstances
This is due to the combined limitations of the edge estimation and TIN construction algorithms
  Could be overcome with further work
  Is a result of phasing out edge optimisation (original assumption: edges will be near-perfect)

## Slide 27: Assumptions regarding accuracy
We are building “road surface DTMs” and interpolating in them
Ground point classification assumed to be perfect
Road slope and ruggedness assumed to be negligible
Sampling density assumed to be high enough not to affect accuracy
 Only the theoretical, propagated error matters
“… while guaranteeing optimal and quantifiable accuracy and completeness?”
Final results and accuracy
Notes: Ultimate assumption is: we are effectively constructing DTMs from Lidar data
Lidar data has been ground filtered nearly perfectly
Road slope and ruggedness assumed to be negligible (smooth, relatively flat surfaces)
Sampling density is high enough to describe the surfaces well
  This is very much the case in general, as diagram shows
 Output elevation accuracy can be determined via theoretical error propagation alone
Highlighted the relevant part of the main research question

## Slide 28: Theoretical accuracy quantification
WVK #600127973
Sampling density drops below minimum
Using a density threshold of 3 points per m2
Local sampling density is measured in the TINs
Generally, violations only occur in data gaps
Output elevation accuracy is around 5.3 cm at 2 STDs
Mean sampling density is 14-27 points per m2 in my testing datasets
Final results and accuracy
Notes: Theoretical error in TIN-linear interpolation roughly constant
  Because of the absence of steeply sloping triangles
  Output elevation accuracy thus constant, and fully determined by input accuracy
Sampling density in TINs remains high almost everywhere, where there is AHN3 coverage

## Slide 29: DTB-related differences
Commercial implementation prioritises DTB unconditionally
However, outdated elevation measurements are common in DTB
  In part, can be explained with subsidence
Differences in the range of 0.1 to 1 m are found in my testing datasets
Observable in comparisons wherever commercial program uses DTB
Significant disagreement between AHN3 and DTB
Comparison with commercial results
Notes: Moving on to the comparison with the commercial results
The primary source of disagreement is related to DTB
  DTB contains lots of outdated elevation data
  The commercial implementation always prioritises DTB in the case of motorways
  These differences are carried over directly into the two sets of results
Hypothesis is that this is ultimately due to subsidence
  Other factors may also be partly responsible
RMSE values between 1 to 15 cm where agreement is good
RMSE values above 50 cm common where DTB is very outdated
Commercial solution makes better use of DTB, because it is specialised to it

## Slide 30: Occlusion-related differences
Commercial implementation does not handle occlusion explicitly
It assumes that DTB exists where AHN3 does not
Where this is violated, it produces large positive outliers
Elevation difference between road surfaces
“Hanging bridge” due to DTB
Comparison with commercial results
Notes: Commercial implementation has no explicit means of dealing with occlusion
Elevations are grossly overestimated where there is occlusion…
  …wherever DTB is missing on motorways
  …always in the case of provincial roads
As shown, the profile simply jumps to the elevation of the bridge
  This is because here the commercial implementation interpolates in infilled AHN3 DTM gaps
The academic pipeline deals with these issues effectively, even where DTB is absent
Commercial solution works without a scaling solution

## Slide 31: Concluding remarks
Pipeline can transpose NWB to 3D via AHN3 and DTB
AHN3 was found to be very useful
DTB should be improved significantly, or replaced by another dataset
NWB’s georeferencing issues caused some headache
Active contour optimisation was found to be unsuitable
The completeness of the generated TINs could be improved
Certain parts of the pipeline could be skipped conditionally
It would suffice to insert far less points into the TINs
For full scale rollout, a scaling solution still needs to be developed
Pipeline is well-documented, source code is available open-source
Conclusions
Notes: Pipeline can transpose NWB to 3D via AHN3 and DTB
  5-10% interpolated linearly, another few percent via DTB
  Rest can be regarded accurate, compliant with noise regulations (< 20 cm at 2 STDs)
AHN3 was found to be suitable for this project, but not DTB
  DTB’s issues should be resolved, or better still, it could be replaced with an MLS dataset
NWB’s georeferencing issues caused some headache, it should be improved
  NDW is already working on it, my thesis contains a comparison
(Basic) active contour optimisation is not suitable to this application
  And is not recommended for future work
The completeness of the generated TINs could be improved via additional work
Certain parts of the pipeline could be skipped conditionally, where they are not necessary
  I.e. were preliminary elevations are accurate enough
  This could improve runtimes considerably
Less points should be inserted into the TINs
  Somewhere slightly above the minimum sampling density would suffice
For full scale rollout, a scaling solution still needs to be developed
Pipeline is well-documented, source code of the implementation available open-source

## Slide 32
Thank you for your attention!
&
Thank you for all your support throughout my graduation year!
Constructing a digital 3D road network for The Netherlands
Notes: Thank you for your attention, and I would like to thank my mentors and family for their help and support throughout my graduation year.

## Slide 33
Questions
Constructing a digital 3D road network for The Netherlands
Notes: We can now move on to any questions you may have.